Changes in the program version 19.0 compared with the 18.0 program version

1. The report “Passport for the product” was corrected. If уou have edited the template of this report in the program, then you need to take into consideration this fact because if you upgrade the program, report templates, edited by the user, aren’t updated.

2. Now when calculating roller shutters side caps “SF45/*u B” is a higher priority than the rest of the caps.

3. Now when calculating roller shutters with the types of drives: “Corduroy”, “Ribbon” or “Cord”, the choice of the side caps “SF45/*u B” is allowed.

4. Now when calculating roller shutters with the basic profile: “AEG56”, “AEG56/P”, “AEG56m” or “AEG56m/P”, the choice of the side caps “SF45/*u B” is allowed.

5. Now when calculating roller shutters side caps “SF45/205u-B” it is allowed to select the caret “RC205“.

6. Now when calculating roller shutters side caps “SF45/*u-B” it is allowed to select the guides “TG/U” and “BG/U”.

7. Now, if in the process of calculating roller shutters side caps  ”SF45/137u-B” are selected, the selection of pulleys “TP125“ and “TPC125” is prohibited.

8. Now when calculating the combined systems instead of side caps “SF*a” the side caps “SF45/*u” should be selected.

9. The new main profiles: “AR/41T“ and “AR/41TN“ are included in the program.

10. The new actuators: “AM0/06-28R“, “AM0/10-17R“, “AM1/10-15R“, “AM1/20-15R“, “AM1/30-15R“, “AM1/40-15R“ and “AM1/50-12R“ are included in the program.

11. The new remotes: “AT-1“, “AT-1S“, “AT-15“ and “AT-15S“.are included in the program.

12. Now when calculating roller shutters the choice of the remote “AT-4B” is allowed.

13. The new guide rails: “GR75x27/SI“ and “GR75x27/SE“ were included in the program.

14. For the capsule “APB102/B” the value of the parameter “Capacity” changed: from 120 kg to 90 kg.

15. The format of xml file that was used for export-import of roller shutter orders changed: the new attributes was added - “ID_Name_By_“, “ID_Artnumber_By_“, “ID_Name_By_Without_P_“, “ID_Artnumber_By_Without_P_“, “ID_P_By_“, “ID_Name_Ru_“, “ID_Artnumber_Ru_“, “ID_P_Ru_“, “ID_Name_Ua_“ and “ID_Artnumber_Ua_“. These attributes were introduced instead of the outdated attribute “Name_“ and “Artnumber_“ (see Help).

16. The format of xml file that was used for export-import of roller shutter orders changed: the new attributes was added -“Drive_Artnumber_“ and “Capacity_“ (see Help).

17. The format of xml file that was used for export-import of roller shutter orders changed: the new attributes was added - “Wind_Speed_“ (see Help).

18. The algorithm of calculating the length of the tube for roller shutters with “KU40” cap and “TPC90” or “TPC125” pulley corrected.

19. New end slat profiles “ESU/77U“ and “ESU/77UI” added.

20. Calculation of roller shutters with “GR90x34*”guide rails and choice of “SP/77-MSM“ and “SP/77-MSW“ side locks prohibited.

21. When calculating roller shutters with “AEG84” curtain profile it is possible to choose “RT108x3,6” tube.

22. New movable carriage “RC360/108“ added.

23. Bugs were fixed.